## Slide 1: Solid Waste in Pit Latrines: The Case of Lusaka, Zambia
Aubrey Simwambi

## Slide 2: Findings
Case study approach through:
Measuring solid waste in pit latrines
Analysis of 10004 household surveys
Analysis of field tests on pit emptying equipment:
  Gulper, Flex X, eVAC _MK3 and Modified garden tools
Surveys with faecal sludge service teams
80% HH use PL and 20% use flush systems
Minimum 1 % SW in all locations end up in PL
150kg SW/m3 emptied sludge in areas with poor SW management services (30% of SW could be thrown into pit latrines in areas lacking services)
Study Design

## Slide 3: Effects of Solid Waste on Faecal Sludge Emptying, Treatment and Disposal
Increases pit emptying time more than two times due to:
    Need for sludge dilution and pit latrine puncturing
Increases failure of innovative sludge emptying technologies:
    Due to solid waste clogging (all pumping technologies need high suction power)
Increases cost of treatment of sludge
    Extra personnel and longer operation times
    About 5% of income is used in disposing solid waste at the treatment plant ($140 is spent monthly in transporting solid waste to the dumpsite)
Increases risk to public health after dumping the solid waste at the disposal site
Affects the use of dry sludge as a soil conditioner

## Slide 4: Lessons
Solid Waste is disposed mostly by HH lacking solid waste management options
High amounts of waste are prevalent in pit latrines as compared to flush systems
MHH products are the prevalent solid waste found in latrines
High need of O&M of OSS facilities (an average containment unit fills up every three years)
High risk of contamination of the operators

## Slide 5: Recommendations
Countries need laws and standards for sanitation systems and they must be adequately enforced
Community awareness on SWM must be enhanced and coupled with waste collection services
SWM must be planned for in future FSM projects
Monitoring mechanisms of solid waste service providers
Small bore interface units should be promoted and encouraged